## Slide 1
Timing Analysis of Safety-Critical Automotive Software: The AUTOSAFE Tool Flow
2 Indian Institute of Technology (IIT) Kharagpur, Computer Science and Engineering (CSE)
4 Tata Research Development and Design Centre (TRDDC)
1 Technische Universität München,
Real-Time Computer Systems (RCS)
3 INCHRON GmbH
M. Becker1, S. Mohamed2, K. Albers3, P.P. Chakrabarti2, S. Chakraborty1, P. Dasgupta2, S. Dey2, R. Metta4

## Slide 2: Outline
Introduction
Motivation and Goals
AUTOSAFE flow
  A. From High-Level Specification to Task Mapping
  B. Timing Analysis
  C. Automata Generation and Formal Verification
  D. Closing the loop
Example
Conclusion

## Slide 3: Introduction
Currently: automotive architectures getting complex:
  Hardware: 50-100 ECUs, numerous sensors and actuators, kilometers of cabling, ...
  Software: ≈100M lines of code, many safety-critical functions
  More functionality, more interfaces, much more software
  Testing becomes infeasible!
  How to guarantee that the software is „correct“?

## Slide 4: Motivation and Goals
Co-design of real-time control – typical design flow
  Requires analysis and optimisation skills from multiple disciplines
    Control design
    Real-time analysis
    Formal verification
  Tool flows in each realm lacks interface points between each other
Goal: To create an interface between multiple disciplines

## Slide 5: Typical Design Flow
Control design
  Numerous Assumptions
    Negligible delays
    Computation – Instantaneous, Periodic
Real-time analysis
Formal Verification
Several design iterations needed
  Design without any analytic backup
  Hinders Certification
A semantic gap exists between high-level models and their implementation
Goal: To bridge this semantic gap
High-level Model
Control Performance satisfied
Code Generation
Implementation
Execution Time satisfied
Performance not met
Low-level Platform Model
Response Time satisfied
Motivation and Goals

## Slide 6: AUTOSAFE Flow - Overview
High-level Model
Control Performance
satisfied
Code Generation
High-level Model
Execution Time satisfied
Performance criteria satisfied
Low-level Platform Model
Response Time satisfied
Implementation
Timing Information
Performance criteria not satisfied

## Slide 7: AUTOSAFE Flow

## Slide 8: A. From High-Level Specification to Task Mapping
High-level specification
  Functional behaviour of the system
  Timing constraints
Functional modeling of the system
  Tools like MATLAB Simulink
Control theoretic analysis
  Generate formal properties (control performance specification)
Generate C code
Modeling system architecture
Mapping
  Binding of functional parts to the architecture blocks

## Slide 9: From High-Level Specification to Task Mapping
Example: ABS
  Performance specification
    Car shall stop within a certain distance when the brakes are applied
  Functional specification
    Regulate brake pressure to keep slip at an optimal value (20%)
  Timing constraint
    Threshold for fresh or stale sensor data
  Control theoretic analysis
    Quantify freshness in terms of (m,k)-firm deadline [1]
      m out of k successive runs meet deadline
Fig: Anti-lock braking system with distributed sensors and controller
[1] Hamdaoui, Moncef, and Parameswaran Ramanathan. "A dynamic priority assignment technique for streams with (m, k)-firm deadlines."
Computers, IEEE Transactions on 44.12 (1995): 1443-1451.

## Slide 10: B. Timing Analysis
Goal: predict safe upper bound for end-to-end timing of implementation (incl. scheduling, bus arbitration, etc.)
  A) task-level timing analysis  worst-case execution time per task
  B) system-level timing analysis  compose tasks via shared resources

## Slide 11: Timing Analysis: Task Level
Scheduling diagrams for each ecu
ECU 1
ECU 2
Controller ECU
Sensor 1
task
Sensor 2
task
t
t
Bus
t

## Slide 12: Timing Analysis: Task Level (AutoGen [5])
1. Extract
Control flow
source
Based on explicit-state model checking
Idea: work at source level, allows better abstractions
Problem: differences in control flow between source and binary
„backtranslate“ differences & timing
Slicing and abstraction
Ask MC for timing
 WCET estimate
2. Cross-Compile
binary
3. Extract
Control flow
3. Extract
timing
flow
differences
source
w/ timing
4.
compare
5.
Translate
Binary flow to source
abstract
source
w/ timing
Model checker
6. Slicing & abstraction w.r.t. timing
7. Timer <= X
8 paths?
Yes  WCET <= X
no
[5] Bokil, Prasad, et al. "Automatic test data generation for c programs."
Third IEEE International Conference on Secure Software Integration and Reliability Improvement, SSIRI 2009.

## Slide 13: Timing Analysis: System Level (chronVAL [6])
(l, u)
(l, u)
(l’, u’)
(l’, u’)
RTC
Real-Time Calculus (RTC) [2]
Architectural nodes: buses, ECUs, etc.
Each node manipulates a stream of incoming tasks
Nodes have capacities according to their policy
Needs WCET
 bounds for end-to-end delays
arrival
curve
service
curve
[2] Samarjit Chakraborty, et al. "A General Framework for Analysing System Properties in Platform-Based Embedded System Designs." DATE. Vol. 3. 2003.
[6] Anssi, Saoussen, et al. "chronVAL/chronSIM: A Tool Suite for Timing Verification of Automotive Applications." Proc. Embedded Real-Time Software and Systems, ERTS (2012).

## Slide 14
Abs on architetcure :: RTCs generated
ECU 1
ECU 2
Controller ECU
Bus
Sensor 1
task
Sensor 2
task
αl={(0,0), (10,1), (20,2),..}
αu={(0,1), (10,2), (20,3),..}
αl = {(0,0), (20,1), (40,2),..}
αu = {(0,1), (20,2), (40,3),..}
αl={(15.34,1), (25.34,2), (35.34,3),..}
αu={(0,1), (4.66,2), (14.66,3),..}
αl = {(26.29,1,0),(30.29,2,0),(46.29,3,0),…}
αu = {(0,1), (1.11,2), (11.11,3),..}
WCRT = 5.4
BCRT = 1.11

## Slide 15: Example: ABS

## Slide 16: C. Automata Generation and Formal Verification
High-level timed automata model of the system
  Event or task generating automata
    Uses system level timing analysis results – RTC curves
  Task automaton
    Uses task level timing analysis results – WCET
    Tracks task generation, execution and completion
  Scheduler automaton
    To specify tasks’ scheduling policy
  Resource automaton
    Models and simulates system architecture
  Observer automaton
    Quantifies the parameters for verification
Formal verification using UPPAAL [3].
[3] Behrmann, Glenn, et al. "UPPAAL 4.0." IEEE Third International Conference on Quantitative Evaluation of Systems, QEST 2006.

## Slide 17: C. Automata Generation and Formal Verification
ABS properties
For time threshold = 4 s, the maximum (m,k)-firm tolerance for sensor1 data = fresh and sensor2 data = stale is (4,5)
For time threshold = 6 s, the (m,k)-firm tolerance for both sensor data = fresh, does not go below (8,10)
RTC  TA
Timed event Generation satisfying RTC is easier
Abstractions of the system can be easily represented
Formal verification tools available

## Slide 18: Example: ABS
Query: If m is reachable?

## Slide 19: D. Closing the loop
Properties are satisfied
  Formal guarantee provided by the tool flow
Property violations
  Counterexample trace
    If spurious?
      Modify respective RTC curves
  Re-execute tool flow like CEGAR loop [4]
[4] Clarke, Edmund, et al. "Abstraction and counterexample-guided refinement in model checking of hybrid systems."
International Journal of Foundations of Computer Science 14.04 (2003): 583-604.

## Slide 20: Conclusion
AUTOSAFE flow – an integrated approach to system design
  An interface between different realms
    Control designer species the control law
    Embedded systems engineer comes up with implementation mapping
    Verification engineer checks for target property
Co-design of real-time control made easier
Automating model refinement using CEGAR loop is part of future work

## Slide 21: References
Hamdaoui, Moncef, and Parameswaran Ramanathan. "A dynamic priority assignment technique for streams with (m, k)-firm deadlines." Computers, IEEE Transactions on 44.12 (1995): 1443-1451.
Samarjit Chakraborty, Simon Künzli, and Lothar Thiele. "A General Framework for Analysing System Properties in Platform-Based Embedded System Designs." DATE. Vol. 3. 2003.
Behrmann, Glenn, et al. "UPPAAL 4.0." IEEE Third International Conference on Quantitative Evaluation of Systems, QEST 2006.
Clarke, Edmund, et al. "Abstraction and counterexample-guided refinement in model checking of hybrid systems." International Journal of Foundations of Computer Science 14.04 (2003): 583-604.
Bokil, Prasad, et al. "Automatic test data generation for c programs." Third IEEE International Conference on Secure Software Integration and Reliability Improvement, SSIRI 2009.
Anssi, Saoussen, et al. "chronVAL/chronSIM: A Tool Suite for Timing Verification of Automotive Applications." Proc. Embedded Real-Time Software and Systems, ERTS (2012).

## Slide 22: THANK YOU !!! Sajid Mohamed sajidm@atdc.iitkgp.ernet.in