## Slide 1: The IMOCO4.E reference framework for intelligent motion control systems
ETFA 2023
12 September, Sinaia, Romania
Sajid Mohamed, sajid.mohamed@itecequipment.com

## Slide 2: Intelligent motion control systems
Critical in modern industrial environments that require precise and complex motion control
Integrates smart sensors, intelligent algorithms, novel computing platforms and smart actuators*
Smart, Intelligent – using AI
Prominent in many industrial domains
Computing Platform
Intelligent algorithms
)
)
Smart Sensor
Smart Actuator
)
*Sajid Mohamed, “D2.3 Overall requirement on IMOCO4.E reference framework,” Zenodo, 2022.
Challenge
Smart integration of intelligent motion control systems with commercial and industrial systems
Notes: First, A brief background on intelligent motion control systems.
Critical in modern industrial environments requiring precise and complex motion control.
They integrate smart sensors, intelligent algorithms, smart actuators and computing platform.

## Slide 3: Challenge of smart integration
Complex task requiring
  significant domain expertise
  industrial ‘know-how’ of processes
  resilient adaptation for various engineering phases
Advancements in AI, big data and digital twin approaches amplify this challenge
  Increased complexity
  Necessity to integrate these novel approaches with brownfield systems
  A standardized integration approach considering novel methods lacking
Challenging for start-ups, SMEs and academic partners to develop commercial platforms seamlessly integrating with brownfield systems

## Slide 4: Proposed solution
The IMOCO4.E reference framework
  a generic platform for
    designing,
    developing, and
    implementing
    novice and complex motion-controlled industrial systems
  refinements and instantiations for different IMOCO4.E industrial cases are also provided

## Slide 5: IMOCO4.E General Info
Acronym: IMOCO4.E
Full name: Intelligent Motion Control under Industry4.E
Coordinator: Sioux Technologies B.V.
GA No.: 101007311 - H2020-ECSEL-2020-RIA
Start date: 1st September 2021
Duration: 36 months
Consortium: 46 Partners from 13 countries
Project Leader: Mr. Arend-Jan Beltman
Arend-Jan.Beltman@sioux.eu
www.imoco4e.eu
@IMOCO4E
@IMOCO4E
👨‍💼
✉
🌐
Connect and find more here:
~31 M€ Total Costs

## Slide 6: The 13 IMOCO4.E Cases
Demonstrators
Demo 1: Shaver blades
Lead: Philips Consumer Lifestyle, NL
Demo 2: Plastic molding
Lead: Edilásio, PT
Demo 3: Warehouse logistics
Lead: Still, DE
Demo 4: Cosmetics production
Lead: Madara Cosmetics, LV
Use Cases
Use case 2: CNC for integrated machine
tool and robot control
Lead: Fagor Aotek, ES, and Tekniker, ES.
Use case 1: Industrial drive for smart mechatronics applications
Lead: Gefran, IT
Use case 3: Tactile Robot Teleoperation
Lead: Tyndall National Institute, IE
Use case 4: Advanced and Intuitive
robot control and programming control
Lead: University of West Bohemia, CZ
Pilots
Pilot 1: Tissector
Lead: Sioux, NL
Pilot 2: Semiconductor production
Lead: ITEC B.V., NL
Pilot 3: High speed packaging
Lead: CRIT, IT
Pilot 4: Healthcare robotics
Lead: Philips Medical Systems, NL
Pilot 5: Mining/tunneling robotic boom
Manipulator Lead: Normet, FI
Pilots | Applications defined at the machine level
Demonstrators | Applications defined at the industrial production-line level
Use Cases | Partial applications on commercial productions of motion control ecosystem

## Slide 7: The benefits (some of the expected results per case)
50%
Testing time reduction by using Digital Twins (Pilot 5)
10%
Reduction of accidents in Warehouse logistics (Demo 3)
10%
Increase of machine speed/ production rate (Pilot 2, 3)
20-40%
Reduction of time-to-market (Pilot 4)
60%
Reduction of the length of the control loop (Demo 4)
Energy consumption reduction by optimizing machine performance (Demo 3)
(Demo 3)
5%
30%
Reduction of material consumption (Pilot 5)
10%
Increased resource utilisation and reduction of waste (Pilot 3)
95%
Increased number of productive hours/day
(Pilot 4)
50%
Reduction of commissioning service/time of new modules to market
(All Pilots)
September 11, 2023
7

## Slide 8: Methodology
Identifying shortcomings from the state-of-the-art reference architectures [1]
Identifying the needs for future smart production from the mechatronics and robotic point-of-view [2]
Gathering and characterizing the brownfield architectures of the industrial cases from IMOCO4.E consortium
First iteration of the requirements [3] and specifications of the IMOCO4.E concepts – layers, BBs, P/D/UCs
Adhere to the guidelines of IMOCO4.E methodology [4] and toolchains
Gathering and characterizing the greenfield reference architectures from industrial partners
[1] Hans Kuppens, “D2.1 State-of-the-art methods in Digital Twinning for motion-driven high-tech applications,” Zenodo, 2021.
[2] Matias Vierimaa, “D2.2 Needs for future smart production in Europe from the mechatronics and robotic point of view,” Zenodo, 2022.
[3] Sajid Mohamed, “D2.3 Overall requirements on IMOCO4.E reference framework,” Zenodo, 2022.
[4] Hans Kuppens, “D6.1 Guideline of IMOCO4.E methodology and toolchains,” Zenodo, 2022.

## Slide 9
The IMOCO4.E reference framework

## Slide 10: The IMOCO4.E reference framework
Overview
Architecture viewpoint
Data management viewpoint
  A brief section on model management
AI viewpoint
Digital twin viewpoint
Refinements for P/D/UCs
From all 13 industrial cases

## Slide 11
Layer 4: digital twin and
AI analytics
Layer 3: system behaviour
Layer 1: sensors/actuators
Layer 2: (de)centralized controllers
…
Machine 1
Machine n
Machine-of-Interest
Interfaces
Edge platform(s)
SW + HW
Sensors
Motion control platform(s)
Motion control platform(s)
Interfaces
Interfaces
Interfaces
Motion control platform(s)
Central platform
Monitoring
Edge processing
Predictive maintenance
Monitoring
Feedback control
Process control
Tuning
Feedforward control
Predictive maintenance
Status monitoring
Diagnostics
SAP/ERP/MES/SCADA
Real-time communication interface(s)
Communication interfaces
Actuators
Server (IT) infrastructure
Smart I/O
Control
Behaviour
Smart I/O
Control
Behaviour
Data storage
AI analytics platform
AI Analytics Aggregation
Digital twin platform
Digital Twin Aggregation
(DTA)
Digital object
Comparitor
Digital object adapter
Decider
Digital object space
Message broker
Persistent storage
Data ingestion
Cyber-security
System administration
Monitor UI
(Re)Trained network
Labelling
(Re)
Training
Dataset
Synthetic/ Augmented Data
Architecture viewpoint

## Slide 12: Data management viewpoint

## Slide 13
Layer 3: system behaviour
Layer 1: sensors/actuators
Layer 2: (de)centralized controllers
Layer 4: digital twin and
AI analytics
Other sensors/ actuators/ platforms
BB4: Real-time platform
Motion control platform(s)
Central platform
BB2: High speed vision-in-the-loop
BB1: SoC/ FPGA platforms
BB3: Novel sensors
BB7: High speed servo drives
BB10: Motion/ Path planning, collision avoidance & navigation
BB5: control configuration & diagnosis
BB8
AI analytics and training instance
BB9
Data
Deploy
trained network
Infrastructure
Tools
Deployment
BB5: smart control algorithms
AI analytics aggregation
Instance data from other machines/systems
AI analytics instance from other machines/systems
BB6: Algorithms for condition monitoring, predictive maintenance and self commission
Deploy
Deploy
Big Data Repository
Distributed Messaging System (DMS)
Data ingestion
Cyber-security
Data visualisation
Dataset
Synthetic/ Augmented Data
Labelling
(Re)
Training
(Re)Trained
Network
Field Gateway Proxy
TSN platform
Notes: A distinction is made between 1. Hardware, 2. Software and 3. platforms (hw + sw + comm)

## Slide 14
Design
Manufacturing
Services
Retire
Next
cycle
Physical entity
AI platform
Data
AI modelling and training
AI inference optimization
AI analytics and services
Machine prototype
Assembled machine
Machine operation
Monitoring
Deployment
Deployment
Process optimisation
Sensing
Sensing
AI Instance

## Slide 15
Layer 3: system behaviour
Layer 1: sensors/actuators
Layer 2: (de)centralized controllers
Layer 4: digital twin and
AI analytics
Other sensors/ actuators/ platforms
BB4: Real-time platform
Motion control platform(s)
Central platform
BB1: SoC/ FPGA platforms
BB2: High speed vision-in-the-loop
BB3: Novel sensors
BB7: High speed servo drives
BB10: Motion/ Path planning, collision avoidance & navigation
BB5: control configuration & diagnosis
BB8
AI analytics and training instance
BB9
Data
Infrastructure
Tools
Deployment
BB5: smart control algorithms
AI analytics aggregation
Instance data from other machines/systems
AI analytics instance from other machines/systems
BB6: Algorithms for condition monitoring, predictive maintenance and self commission
Big Data Repository
Distributed Messaging System (DMS)
Data ingestion
Cyber-security
Data Visualisation
Dataset
Synthetic/ Augmented Data
Labelling
(Re)
Training
(Re)Trained
Network
DT platform
Digital twin instance
Digital twin aggregation
Digital twin instances of other machines
Digital object
Comparitor
Digital object adapter
Decider
Field Gateway Proxy
TSN platform
Notes: A distinction is made between 1. Hardware, 2. Software and 3. platforms (hw + sw + comm)

## Slide 16
Design
Manufacturing
Services
Retire
Next
cycle
Physical entity
DT platform
Data
Digital twin virtual models
Digital twin prototype
Digital twin instance
Machine prototype
Assembled machine
Machine operation
Digital Twin Instance
Optimisation
Specifications
Parameters
Sensing
Control
Monitoring
Predictive maintenance

## Slide 17
Example refinements

## Slide 18: Pilot 4 – Philips Medical Systems
Healthcare robotics

## Slide 20: Demonstrator 3

## Slide 21: Use case 4 – collaborative robotic platform
Power cables
Encoder cables
I/O
Encoders
Hardware
I/O
7x AMC2 servo controllers
AMC2 controller
Low-level drive control (torque/velocity/position loop)
Controls robot motors and brakes
Interfaces for I/Os (e.g. inertial or force/torque sensors)
Layer 4
Cloud Server
EtherCAT
COLLABORATIVE ROBOTIC PLATFORM
Machine Smart I/O
Machine Control
Machine Behaviour
Machine Smart I/O
Machine Control
Machine Behaviour
…
Machine 1
Machine n
TCP/IP – REST/MQTT/OPC UA
Data Storage
Monitor, Maintenance & drive commissioning system
Motor
Industrial PC (IPC)
TCP/IP
Industrial Router
BB5
BB7
BB6
Brake

## Slide 22: Conclusion
IMOCO4.E Reference Framework for edge-to-cloud intelligence
A framework for smart integration of intelligent motion control systems with commercial and industrial systems
Intelligent motion control systems will be:
01
SMARTER
02
  FASTER
03
RESILIENT
06
  Highly configurable
05
  HIGHLY RELIABLE
04
  HIGHLY ACCURATE
September 11, 2023
22

## Slide 23
Thank you! Questions?
Find more:
www.imoco4e.eu
Connect with us:
@IMOCO4E
@IMOCO4E